## Slide 1
INTERCEPT® Blood System for Platelets Pathogen Reduction System
(Psoralen/UVA Treatment)
Nursing Training Module
MKT-EN 00422-08 v1.0

## Slide 2
When you think of the risks associated with blood product transfusions, what
comes to mind?

## Slide 3: Do You Think About the Risk of These Viruses Being Potentially Transmitted By Transfusions?
Hepatitis C
HIV
Courtesy CDC Public Health Image Library
Courtesy CDC Public Health Image Library

## Slide 4: Do You Think About the Risk of CMV Transmission?
Platelets that are either leuko-reduced or CMV-seronegative are often referred to as “CMV-safe” or “CMV Negative” by hospital transfusion services
“CMV-safe” or “CMV Negative” units may still carry a 2.4%1 - 6.5%2 risk of CMV transmission
Bone Marrow Transplant (BMT), pediatric, and neonate patients are most susceptible to transmission of CMV
  15-20% mortality rate among BMT patients that get CMV3
  CMV pneumonia is associated with mortality rate of 80-90%3
1 . Bowden et al. Blood. 1995; 86(9):3598-3603.
2. Wu et al. Transfusion. 2010; 50:776-786.
3. Sable CA, et al. Clin Infect Dis. 1994;18:273-281.
Notes: Vamvakas EC. Transfus Med Rev 2005;19:181-99.

## Slide 5: Do You Think About the Risk Of Emerging Pathogens such as Dengue, Zika, or Yellow Fever...?

## Slide 6: Do You Think About the Risk of Babesia Transmission in a Transfusion?
Babesia microti, a tick-borne parasite, can cause a malaria-like illness. Although healthy children and adults with Babesiosis are often asymptomatic, the infection may be fatal in neonates, the elderly, and immune-compromised individuals
Babesia cases are observed year-round and have steadily increased over the past several years in the United States, especially in the northeast
Babesia contamination of red blood cells is responsible for the highest percentage of transfusion-related infection fatalities in the United States1*
In May 2019, FDA issued a guidance requiring year-round NAT testing for Babesia of all collections in 14 northeastern states and Washington DC or pathogen reduction for plasma or platelets collections2
Transfusion News. FDA recommends screening blood donors nationwide for Babesia. Available at: http://transfusionnews.com/2015/05/22/fda-recommends-screening-blood-donors-nationwide-for-babesia/. Accessed July 24, 2016
FDA. Recommendations for Reducing the Risk of Transfusion-Transmitted Babesiosis: Guidance for Industry. In: U.S. Department of Health and Human Services FDA, ed. Silver Spring, MD: Center for Biologics Evaluation and Research; May 2019.
* INTERCEPT Blood System for RBC is in development and not approved for commercial use.

## Slide 7: Platelet Transfusions
Each year 2.5 million platelet units are transfused to patients in the U.S.1
Many of these patient populations are compromised given their disease states (oncology, immunocompromised patient)
Platelets are transfused throughout the hospital
Ellingson KD, et al. Transfusion 2017;57 Suppl 2:1588-98.
Chart: 
| Peds/Neonates | Transplant (Solid Organ) | Trauma/ER | ICU (Med & Surg) | Gen Medicine | Gen Surg | Cardiac Surg | Hem/Onc/BMT | All Other
 | 0.079 | 0.024 | 0.034 | 0.13 | 0.128 | 0.051 | 0.087 | 0.436 | 0.031

## Slide 8: Pathway to Platelet Use: Standard Platelet Collection and Distribution
Donor
Blood Center:
Bacterial Culture
(aerobic only)
Viral Testing
12-24hr hold for results
Sent to Hospital Blood Bank
Most donations are split into 2-3 platelet units
Platelet Unit
Viruses
Bacteria
Parasites
Leukocytes
Platelet donation, like any tissue or organ donation, carries with it the host’s condition
Regardless of physical symptoms, the donor may carry any number of pathogens, for example even a healthy donor is bacteremic twice a day when they brush their teeth1
Pathogens
1. Bhanji, Pediatric dentistry 2002;24:295-9
Notes: 1. Bhanji S, Williams B, Sheller B, Elwood T, Mancl L. Transient bacteremia induced by toothbrushing a comparison of the Sonicare toothbrush with a conventional toothbrush. Pediatric dentistry 2002;24:295-9.

## Slide 9: Pathway to Platelet Use: Standard Platelet Collection and Distribution
Hospital:
Blood products are stored at the hospital blood bank
Platelets are ordered for patient use
Platelets are stored for up to 5 days at room temperature on a rocker in the blood bank
Contamination risks from viruses, emerging pathogens and parasites are largely unknown
During storage time:
Bacteria
Parasites
Remain stable in the platelet unit
Retain infectious risk
Metabolize nutrients, potentially altering pH
Rapid growth potential
Sepsis risk increases with storage time
Empty bag thrown away
Viruses
Remain stable in the platelet unit
Retain infectious risk
Leukocytes
Continue to produce cytokines
Retain transfusion-associated graft-vs-host disease risk

## Slide 10: Are Platelets Safe?
Despite implementation of interventions to mitigate bacterial contamination and reduce associated adverse events (AEs), residual risks remain…
Several recent studies demonstrate that platelets contaminated with bacteria continue to be transfused1–4
Bacterial Contamination Risk
Known/Unknown Viral and Parasite Infectious Risk
~1:1,500-2,500 Units1,6
~1:250-400 Patients5,6*
?
Zika
Yellow Fever
Babesia
Chikungunya
Dengue
Plasmodium
*Assuming 6 platelet units per patient See slide notes: 1. Dumont, 2010; 2. Pearce, 2011; 3. Murphy, 2008; 4. Walther-Wenke, 2011; 5. Kleinman, 2013; 6. Hong, 2016;
How many bacteria are safe to transfuse into your patients?
Notes: Dumont, LJ et al. Transfusion. 2010 Mar;50(3):589–99.
Pearce, S et al. Transfus Med. 2011 Feb;21(1):25–32.
Murphy, WG et al. Vox Sang. 2008 Jul;95(1)13–9.
Walther-Wenke, G et al. Vox Sang. 2011 May;100(4):359–66.
Kleinman, S et al. Transfusion. 2013 Jul;53(7):1603–18.
Hong H, et al. Blood. 2016;127(4):496-502.

## Slide 11: How fast can bacteria grow? Invisible and visible contamination1
The recipient of the first bag had no adverse reaction after the transfusion
Bag 2 failed visual inspection 4 hours after transfusion of Bag 1; re-culturing showed contamination with Enterobacter aerogenes
Not all contamination is visible
Day 0
Day 1
Day 2
Day 3
Day 4
Donation
Bag 1: passed visual inspection, transfused to a patient
Day 5
Platelet unit split and released to hospital as negative for bacterial contamination
Bag 1
visual inspection:
Bag 2
visual inspection:
4hrs
later
Bacterial
Culture
1. Wendel S, et al. Transfusion 2005;45:1241.
Notes: Wendel S, Morato L, Fontão-Wendel R, Toledo R. Double, double, toil and trouble. Transfusion 2005;45:1241.

## Slide 12: Why Is There A Need For Pathogen Reduced Platelets?
FDA HAS INCREASED THEIR FOCUS ON BLOOD SAFETY
Pathogen Reduction (e.g. INTERCEPT® Blood System) is an integral component of US Blood Safety Guidances:
  Bacterial risk control1
  Zika virus risk reduction2
  Babesiosis risk reduction3
Transfusion Services (Hospitals) are also responsible for reducing risk of bacterial contamination in platelets
1.“Bacterial Risk Control Strategies for Blood Collection Establishments and Transfusion Services to Enhance the Safety and Availability of Platelets for Transfusion,” FDA Guidance for Industry, Sept 2019.
2. FDA. Revised Recommendations for Reducing the Risk of Zika Virus Transmission by Blood and Blood Components. FDA Guidance for Industry July 2018.
3. FDA. Recommendations for Reducing the Risk of Transfusion-Transmitted Babesiosis: Guidance for Industry. In: U.S. Department of Health and Human Services FDA, ed. Silver Spring, MD: Center for Biologics Evaluation and Research; 2019.
Notes: 1.“Bacterial Risk Control Strategies for Blood Collection Establishments and Transfusion Services to Enhance the Safety and Availability of Platelets for Transfusion,” FDA Guidance for Industry, Sept 2019.
2. FDA. Revised Recommendations for Reducing the Risk of Zika Virus Transmission by Blood and Blood Components. FDA Guidance for Industry July 2018.
3. FDA. Recommendations for Reducing the Risk of Transfusion-Transmitted Babesiosis: Guidance for Industry. In: U.S. Department of Health and Human Services FDA, ed. Silver Spring, MD: Center for Biologics Evaluation and Research; 2019.

## Slide 13: INTERCEPT® Blood System Summary FDA Approved Pathogen Reduction Technology (PRT)
*Transfusion-Associated Graft vs. Host Disease
**Data for pathogen reduction of Zika virus by the INTERCEPT Blood System, pathogen reduction system, has not been submitted for FDA review.
See slide notes: 1) FDA Guidance for Industry, Sept 2019; 2) AABB, 31th edition, 2018; 3) Package Insert, Cerus 2018 4) FDA Babesiosis 2019; 5) WHO guidance 2016; 6) ECDC Zika 2016; 7) FDA Zika Guidance, July 2018
Industry Guidelines enable use of INTERCEPT as an option in place of certain tests and/or procedures | 
 | The FDA Guidance1 and AABB Standard 5.1.5.22 state that PRT can be used in place of bacterial testing.
 | FDA has approved and AABB Standard 5.19.3.1 allows for INTERCEPT as an alternative to gamma irradiation for the prevention of TA-GVHD*.2,3
 | INTERCEPT provides cytomegalovirus (CMV) inactivation levels3 meeting the AABB Standard 5.19.22 policy requiring methods to reduce CMV transmission risk.
 | Pathogen reduction (e.g., INTERCEPT Blood System) is an FDA recommended option to mitigate Babesia transfusion transmission for the states required to implement a strategy4 The INTERCEPT Blood System is also FDA approved to reduce the risk of T. Cruzi and Plasmodium parasite transfusion transmission.3
 | WHO5, European Centre for Disease Prevention and Control (ECDC)6 and FDA Guidance7 for Zika state that PRT** can be used in place of Zika testing or importing from non-endemic areas.
Bacteria
Emerging Pathogens
Protozoan
Parasites
CMV
T-cells
?
Notes: 1.“Bacterial Risk Control Strategies for Blood Collection Establishments and Transfusion Services to Enhance the Safety and Availability of Platelets for Transfusion,” FDA Guidance for Industry, Sept 2019.
2. “Standards for Blood Banks and Transfusion Services,” AABB, 31th edition, 2018.
3. The INTERCEPT Blood System for Platelets Package Insert, Cerus Corporation; July 17, 2018.
4. FDA. Recommendations for Reducing the Risk of Transfusion-Transmitted Babesiosis: Guidance for Industry. In: U.S. Department of Health and Human Services FDA, ed. Silver Spring, MD: Center for Biologics Evaluation and Research; 2019.
5. “Maintaining a safe and adequate blood supply during Zika virus outbreaks. Interim guidance. WHO, February 2016.
6. “Zika Virus and Safety of Substances of Human Origin,” ECDC, July 2016.
7. FDA. Revised Recommendations for Reducing the Risk of Zika Virus Transmission by Blood and Blood Components. FDA Guidance for Industry July 2018.

## Slide 14: INTERCEPT® Blood System for Platelets Pathogen Reduction System1
There is no pathogen inactivation process that has been shown to eliminate all pathogens. Certain non-enveloped viruses (e.g., HAV, HEV, B19, and poliovirus) and Bacillus cereus spores have demonstrated resistance to the psoralen/UVA light process.
INTERCEPT
Platelet component
Patient
INTERCEPT crosslinks DNA and RNA
to prevent pathogen replication
Enveloped viruses
Non-enveloped viruses
Gram-negative bacteria
Gram-positive bacteria
Protozoa
Spirochetes
Leukocytes
Donor
Donated Platelet
UVA illumination
The INTERCEPT Blood System for Platelets Package Insert, Cerus Corporation; July 17, 2018.
Addition of psoralen
Notes: INTERCEPT Blood System for Platelets [Package Insert]. Concord, CA: Cerus Corporation; 2018.

## Slide 15: How Well Does the INTERCEPT® Blood System Work?
FDA has approved the risk reduction claim of the INTERCEPT Blood System based on the log10 reduction of contamination.
What is a “log” reduction?
  A 4 log10 reduction =99.99% inactivation of contamination
  A 5 log10 reduction =99.999% inactivation of contamination
The next slide shows how effective psoralen/UVA light treatment is on many potential contaminants.

## Slide 16: >4 Logs Reduction with the INTERCEPT® Blood System for Platelets1
The INTERCEPT Blood System for Platelets Package Insert, Cerus Corporation; July 17, 2018.
*PRV: Pseudorabies virus a model for CMV
** There is no pathogen inactivation process that has been shown to eliminate all pathogens.
b = Not tested
c = Based on culture of full platelet unit (300mL)
Viruses | Log Reduction PAS-3/Plasma
HIV-1, cell-associated | ≥5.4/≥4.7
DHBV (model virus for HBV) | ≥4.8/≥4.3
BVDV (model virus for HCV) | ≥4.1/>3.5
HTLV-I | 4.7/b
HTLV-II | ≥5.1/b
West Nile Virus | ≥6.3/>6.3
Chikungunya virus (CHIKV) | ≥5.7/>6.5
Dengue virus (DENV) | ≥4.3/3.6
Cytomegalovirus (CMV), cell-associated | ≥4.9/≥4.2 (PRV*)
Influenza A virus | ≥5.9/b
Bluetongue virus | 5.2/4.4
Adenovirus | ≥4.9/≥5.3
Protozoan Parasites | Log Reduction PAS-3/Plasma
Plasmodium falciparum | ≥6.6/>6.5
Babesia microti | ≥4.9/>4.5
Trypanosoma cruzi | ≥7.8/>8.4
Bacteria | Log Reduction PAS-3/Plasma
Escherichia coli | ≥6.3/>5.9
Yersinia enterocolitica | ≥5.9/>6.3
Klebsiella pneumoniae | >6.2/>6.2
Serratia marcescens | ≥6.7c/>7.1
Staphylococcus epidermidis | ≥6.4/>6.5
Staphylococcus aureus | ≥6.6/≥6.5
Streptococcus pyogenes | ≥6.8c/>6.1
Bacillus cereus (vegetative) | ≥5.5 /≥5.6
Bacillus cereus (spore forming) | 3.7c/b
Clostridium perfringens (vegetative) | ≥6.5/>6.0
Propionibacterium acnes | ≥6.5 />6.7
Treponema pallidum | ≥6.4/>6.3
Borrelia burgdorferi | ≥6.8/>4.1
Leukocytes | Log Reduction
Human T-Cells | 4
Notes: Note that this only covers some of the pathogens inactivated by INTERCEPT

## Slide 17: What is Transfusion Associated Graft vs. Host Disease (TA-GVHD)?
  The donor leukocytes (T-cells) attack the recipient, but the recipient does not attack the donor T-Cells
  Rare but nearly always fatal
  May affect immuno-competent patients more often than thought
  Although criteria exist to determine “at risk” patients, 50% of TA-GVHD cases occur in patients who would not be predicted to be at risk for TA-GVHD by current guidelines for blood irradiation1
Kopolovic et al. A systematic review of transfusion-associated graft-versus-host disease. Blood 2015;126(3):406-414

## Slide 18: What are the Standards for T-Cell Inactivation?
The American Association of Blood Banks (AABB) standard 5.19.3 reads1:
  The blood bank or transfusion service shall have a policy regarding the prevention of transfusion-associated graft-vs-host disease (TA-GVHD)
  Acceptable methods known to prevent transfusion-associated graft-vs-host disease include irradiation and pathogen reduction technology known to inactivate residual leukocytes and that is cleared or approved by the FDA or Competent Authority
  FDA has approved and AABB Standard 5.19.3.1 allows for the INTERCEPT® Blood System to be used as an alternative to gamma irradiation for the prevention of TA-GVHD1,2
“Standards for Blood Banks and Transfusion Services,” AABB, 31th edition, 2018.
The INTERCEPT Blood System for Platelets Package Insert, Cerus Corporation; July 17, 2018.

## Slide 19: Reduction of T-Cells
To a level that prevents TA-GVHD1
Psoralen/UVA processed platelets exhibited a 4 log10 reduction of viable T-cells1
High number of base-pair modifications ensures inactivation of most genes
The INTERCEPT Blood System for Platelets Package Insert, Cerus Corporation; July 17, 2018.
Grass et al. Blood 1998; 91(6):2180-8
Setlow, RB, et al. Irradiation of blood components. Bethesda, MD. AABB,1992 p1.
Gamma irradiation 1:37,000 strand-break: base pair
Psoralen/UVA Platelets 1:831-3 amotosalen adduct formed: base pair

## Slide 20: No Sepsis Cases or Fatalities with INTERCEPT® Blood System Pathogen Reduction System Treated Platelets
 | Conventional Platelets |  | INTERCEPT Platelets | 
Year | Units Transfused (n) | Transfusion Transmitted Sepsis (Fatalities) | Units Transfused (n) | Transfusion Transmitted Sepsis (Fatalities)
2006-131,2 | 2,023,600 | 44 (8) | 153,951 | 0 (0)
20142 | 278,788 | 2 (0) | 26,676 | 0 (0)
20152 | 272,836 | 4 (1) | 33,666 | 0 (0)
20162 | 285,305 | 1 (0) | 21,806 | 0 (0)
20172 | 242,906 | 2 (0) | 66,004 | 0 (0)
2005-143,4,6 | 156,719 | 16 (3) | 130,797 | 0 (0)
20153,4 | 0 | 0 (0) | 36,439 | 0 (0)
20163,4 | 0 | 0 (0) | 38,374 | 0 (0)
20173,4 | 0 | 0 (0) | 37,490 | 0 (0)
20185 | 0 | 0 (0) | 38,947 | 0 (0)
2009-126 | 207,659 | 4 (0) | 110,660 | 0 (0)
20136 | 40,344 | 0 (0) | 29,456 | 0 (0)
20146 | 38,221 | 3 (0) | 28,834 | 0 (0)
20156 | 8,253 | 0 (0) | 57,428 | 0 (0)
20166 | 0 | 0 (0) | 65,501 | 0 (0)
Total | 3,554,631 | 76 (12) | 876,029 | 0 (0)
France
Belgium
Switzerland
France
Cazenave, JP, H Isola, et al., Pathogen Inactivation of Platelets, in Platelet Transfusion Therapy, AABB Press: Bethesda, MD 2013; 19-176
French National Agency for Medicine and Health Product Safety/ANSM, Hemovigilance Activity Reports, 2009–2017.
SwissMedic Haemovigilance Annual Reports, 2005–2018.
Jutzi M. et al. Transfus Med Hemother 2018;45:151-6.
Benjamin et al. Transfusion 2017;57:2946-57
AFMPS Hémovigilance Rapport annuel: Belgium. 2016.

## Slide 21: INTERCEPT® Blood System for Platelets (Psoralen-Treated)
Psoralen Treatment is a proactive approach to mitigating transmission risks of platelet transfusions
Clinical summary for PSORALEN-TREATED platelets:
  Reduces the risk of transmission of known and emerging pathogens
  5-day shelf life
  No age or population restrictions for use1*
  FDA guidance recommended replacement for primary and secondary bacterial culture screening
  FDA approved alternative to gamma irradiation for the prevention of transfusion-associated graft vs. host disease (TA-GVHD)
*see warnings and contraindications slide next
The INTERCEPT Blood System for Platelets Package Insert, Cerus Corporation; July 17, 2018.

## Slide 22: Warnings and Contraindications for Psoralen Treated Platelets
CONTRAINDICATIONS:
Contraindicated for preparation of platelets intended for patients with a history of hypersensitivity reaction to amotosalen or other psoralens.
Contraindicated for preparation of platelet components intended for neonatal patients treated with phototherapy devices that emit a peak energy wavelength less than 425 nm, or have a lower bound of the emission bandwidth <375 nm, due to the potential for erythema resulting from interaction between ultraviolet light and amotosalen.
WARNINGS AND PRECAUTIONS
Only INTERCEPT Processing Sets for platelet components are approved for use with the INTERCEPT Blood System. Use only the INT100 Illuminator for UVA illumination of amotosalen-treated plasma or platelet components. No other source of UVA light may be used. Please refer to the Operator’s Manual for the INT100 Illuminator. Discard any plasma or platelet components not exposed to the complete INT100 illumination process.
Tubing components and container ports of the INTERCEPT Blood System for Platelets contain polyvinyl chloride (PVC). Di(2-ethlhexyl)phthalate (DEHP) is known to be released from PVC medical devices, and increased leaching can occur with extended storage or increased surface area contact. Blood components will be in contact with PVC for a brief period of time (approx. 15 minutes) during processing. The risks associated with DEHP released into the blood components must be weighed against the benefits of therapeutic transfusion.
INTERCEPT processed platelets may cause the following adverse reaction: Acute Respiratory Distress Syndrome (ARDS). An increased incidence of ARDS was reported in a randomized trial for recipients of INTERCEPT processed platelets, 5/318 (1.6%), compared to recipients of conventional platelet components (0/327). Monitor patients for signs and symptoms of ARDS.
Rx only. © 2018 Cerus Corporation. INTERCEPT is a registered trademark of Cerus Corporation.
The INTERCEPT Blood System for Platelets Package Insert, Cerus Corporation; July 17, 2018.

## Slide 23: Hypersensitivity to Psoralens
US Package Insert
  Contraindicated for preparation of platelet components intended for patients with a history of hypersensitivity reaction to amotosalen or other psoralens.
  “Amotosalen” is the name of the specific psoralen used in the INTERCEPT Blood System treatment process
Psoralen treated products have been in routine use in patients in Europe (15+ years) and USA (3+ years) with over 5 million psoralen treated components administered with no hypersensitivity reaction to psoralen reported to date
The INTERCEPT Blood System for Platelets Package Insert, Cerus Corporation; July 17, 2018.

## Slide 24: Hypersensitivity reactions to Psoralens have not been documented to date
Psoralens are present in a wide variety of foods so it is likely most people have ingested psoralens in their diet
More psoralen is consumed in one stalk of celery than used to psoralen treat one unit of platelets1
In addition, the majority of psoralen is filtered out of the platelet unit before it is sent to the hospital blood bank
FOODS RICH IN PSORALEN1 |  |  | 
Anise Seeds | Cilantro | Fennel | Lovage (Leaf Parsley)
Caraway Seeds | Coriander Seeds | Figs | Mustard Seed
Carrots | Cumin Seeds | Grapefruit | Parsnips
Celeriac | Dill | Lemons/ Limes | Root Parsley
Celery | Chevril (French Parsley) | Orange | Turnips
Wagstaff, D.J. Dietary exposure to furocoumarins. Regul. Toxico. Pharmacol. 1991;14:261-272

## Slide 25: Use with Neonatal Phototherapy
US Package Insert1
  Contraindicated for preparation of platelet components intended for neonatal patients treated with phototherapy devices that emit a peak energy wavelength less than 425 nm, or have a lower bound of the emission bandwidth <375 nm, due to the potential for erythema resulting from interaction between ultraviolet light and amotosalen
American Academy of Pediatrics-Clinical Practice Guidelines2
  Recommended spectrum for intensive phototherapy: 430 – 490 nm
  Use special blue tubes or LED light source with output in the visible blue-green spectrum for intensive phototherapy
  Cautionary language around use of halogen lamps (to avoid burns)
  None of the neonatal phototherapy devices approved for market in the US today emit a peak wavelength below 425 nm, and/or a lower bound of the emission bandwidth less than 375 nm3
The INTERCEPT Blood System for Platelets Package Insert, Cerus Corporation; July 17, 2018.
Pediatric Clinical Practice Guidelines & Policies, 16th edition. American Academy of Pediatrics; 2016.
Bhutani et al. Phototherapy to Prevent Severe Neonatal Hyperbilirubinemia in the Newborn Infant 35 or More Weeks of Gestation. Pediatrics 2011; 128(4):e1046-1052

## Slide 26: Warnings and Precautions:
US Package Insert1:
INTERCEPT processed platelets may cause the following adverse reaction: Acute Respiratory Distress Syndrome (ARDS) An increased incidence of ARDS was reported in a randomized trial for recipients of INTERCEPT processed platelets, 5/318 (1.6%), compared to recipients of conventional platelet components (0/327). Monitor patients for signs and symptoms of ARDS.
This effect has not been seen since these results were documented in clinical trial results used for the FDA approval process. This is not a contraindication for use.
A reanalysis of the data was done and found no difference in ARDS between the two patient groups.2
A Phase IV study is being done to re-evaluate the risk of ARDS.
The INTERCEPT Blood System for Platelets Package Insert, Cerus Corporation; July 17, 2018.
Corash, L., et al. Determination of acute lung injury after repeated platelet transfusions. Blood. 2011 117(3): 1014-1020.

## Slide 27: INTERCEPT® Blood System (psoralen treated) Platelets
DIFFERENCES IN PLATELET BAG APPEARANCE
    Bag is 2.8 inches longer, however the platelet volume is the same
    No IRRADIATION Sticker
    INTERCEPT BLOOD SYSTEM embossed across the top of the bag
CONVENTIONAL PLATELET
PSORALEN TREATED
PLATELET

## Slide 28: Administration of INTERCEPT® Blood System (psoralen-treated) Platelets
Platelet dosing and volume of the psoralen-treated platelets are the same as conventional platelet products.
Pre-medication and hang time for psoralen-treated platelets are the same as conventional platelet products.
Patients may receive both conventional platelets and psoralen-treated platelets to fill their transfusion requirements.
Psoralen-treated platelets can be transfused in the same line as conventional platelets.

## Slide 29: INTERCEPT® Blood System (Psoralen Treated) Platelet Labeling
    Labeled as: APHERESIS PLATELETS (PAS-C ADDED) LEUKOCYTE REDUCED
      PAS-C is the solution that the platelets are collected in at the time of donation, if not in plasma
    Note new wording added to label: PSORALEN TREATED
APHERESIS PLATELETS
PAS-C ADDED LEUKOCYTES REDUCED PSORALEN-TREATED
APHERESIS PLATELETS LEUKOCYTES REDUCED PSORALEN-TREATED

## Slide 30: IRRADIATED VS. PSORALEN TREATED Platelet Labeling
An INTERCEPT treated (psoralen treated) platelet unit may be administered when an irradiated platelet unit is ordered.
Psoralen treatment is an FDA approved alternative to gamma irradiation for the prevention of Transfusion Associated Graft vs. Host Disease (TA-GVHD)
NO Rad-SureTM sticker will be present on the psoralen treated platelets
An auxiliary sticker or tie tag as pictured (yellow) may be added to a psoralen treated platelet
PSORALEN TREATMENT of platelets is an FDA approved alternative to GAMMA IRRADIATION of platelets.

